## Slide 1
Init
LoRa Connecting
POWER ON state
SEND_TIME_COMMAND
Send the 't' character by lora to ask for actual time
GET_TIME
Receive the actual time, write RTC with the received time
GET_SENSOR_DATA
TRANSMIT_SENSOR_DATA
RECEIVE_INSTRUCTIONS
WATERING
Get the sensor data and put the values in general variables
Construct the LoRa payload and send it to the server
Receive the watering time from the server and when it should wake up
Start the watering procedure
SET_ALARM_AND_SLEEP
Verify if the next wake up time and if watering is necessary, set the alarm and go to sleep
Main states
Join the LoRa Network

## Slide 2: Other states
Unexpected Flow
Low Battery
Send data to the cloud, so the cloud will give the user an email
Send data to the cloud, so the cloud will give the user an email

## Slide 3: Vectors and comm protocols
Node sends 't'
Server sends time in unix format (4 bytes)
Sensor data transmitted from the node to the server as it follows
lora_payload[0] = ((int)(temperature * 100)>>8)&(0xFF);
lora_payload[1] = (int)(temperature * 100)&(0xFF);
lora_payload[2] = (illuminance)&(0xFF);
lora_payload[3] = (humidity * 100)&(0xFF);
lora_payload[4] = ((counter) >> 8)&(0xFF);
lora_payload[5] = (counter)&(0xFF);
lora_payload[6] = ((int)(debit() * 100) >> 8)&(0xFF);
lora_payload[7] = (int)(debit() * 100)&(0xFF);
lora_payload[8] = ((int)(battery) >> 8)&(0xFF);
lora_payload[9] = (int)(battery)&(0xFF);
Server sends back the next waking time as it follows
Lora_payload[0] = watering_time;
Lora_payload[1] = watering _time;
Lora_payload[2] = watering _time;
Lora_payload[3] = watering _time;
Lora_payload[4] = watering_duration;
Lora_payload[5] = watering_duration;
//should include the watering time and the next wake up time.
Lora_payload[6] = action; //0 just transmit sensor data and fetch instructions, 1 water the plants